## Slide 1: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
The drawbacks of Li-ion batteries
  Unsafety when overcharged; degradation; high sensitivity to temperature.
Introduce the battery management system (BMS)
  Cell balancing; temperature control.
Acquire the SoC and SoH
  State of charge (SoC): the ratio between the saved energy and the total energy in the battery.
  State of health (SoH): the ability of to store energy, correlated to the age of the battery.
The usage of SoC and SoH
  SoH: to predict problems, and to plan replacement.
  SoC: based on SoH, to control the battery.
Targets and Objectives
Notes: SoC and SoH are 2 important infos for BMS.

## Slide 2: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
SoC acquisition
  Direct measurement: open voltage measurement; coulomb counting -
  State and/or parameter estimation: Kalman filters, Luenberger observers and so on.
SoH acquisition
  Number of charging/discharging cycles;
  Charging curves;
  Capacity;
  Internal resistance.
Existing approaches
Notes: And there are several existing approaches to acquire SoC and SoH. This paper is basically based on Luenberger observer to achieve SoC estimation and on the estimate of internal resistance to predict SoH.

## Slide 3: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
The nonlinearity of the mathematical model
  The internal parameters change with time (depending on SoC and/or T);
  Two sets of parameters due to the current direction (charging and discharging).
Apply an adaptive observer to achieve combined estimation
  State estimation: SoC.
  Parameter identification: R0 (related to SoH).
Based on a switching mechanism
  to minimize the transinent peaks
  due to the discontinuity between charging and discharging phrases.
The paper in a nutshell
Notes: This paper introduced a nonlinear model of the battery first. The model is nonlinear because ...
And then they applied an adaptive observer to achieve a joint estimation of state SoC and Parameter R0.

## Slide 4: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Nonlinear equivalent model
Equivalent circuit based model
The input U is the current I;
the output y is the termial voltage.
The states are V1, V2, and SoC respectively,
where V1 and V2 are the transient responce.
The variable parameters are
Rs, Cs, Rl, Cl, ohmic resistance R0, and
open circuit voltage Voc.
Two sets of parameters based on the current direction.

## Slide 5: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Correlation between internal parameters and SoC and T
Nonlinear original model VS nonlinear simplified model
↓ simplify
to correct the output equation and
to update the variable parameters on each iteration
Notes: Because for all the resistances and capacitances they share a common structure, so here we just show the one of R0.
The simplified model has a good approximation of the original one.
The formula for Voc is used to
while the ones for the rest are ...

## Slide 6: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Ageing model (the relationship between SoH and R0)
Begin of Life VS End of Life
Predict the SoH by the estimate of R0
Notes: The ageing model is actually the correlation between SoH and capacity and resistance.
At the end of life,
Based on this, we can predict

## Slide 7: SoC/SoH Estimation by an Adaptive Observer
Adaptive observer
Li, Xiuliang, Qinghua Zhang, and Hongye Su. "An adaptive observer for joint estimation of states and parameters in both state and output equations." International Journal of adaptive control and signal processing 25.9 (2011): 831-842.
Notes: The adaptive observer is designed for linear systems in structure like this. So based on it, the observer can achieve the joint estimations of state x and parameter \theta. The additional state \upsilon is introduced to make the linear combination x - \upsilon * \theta converges to zero as time goes to infinity. And the gain matrix K can be calculated by solving the Riccati equation written on the right hand. It will make the observer converge in an optimal way, which shares the same idea as the LQR controller. The matrix V, W plus \gamma can be assigned by trial and error. Finally, the matrices can be written based on the mathematical model we introduced before. But it’s worth noting that in order to put R0 into the parameter vector \theta, we need to reconstruct the output equation a little bit. Which is that we assign current as \psi but not U.

## Slide 8: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Switching observer
Switcing mechanism
To minimize the transinent peaks in estimation curves;
2 observers with the same structure are used (charging/ discharging);
The estimate of states are updated continuously;
while the one of parameter is saved and updated in each observer individually.

## Slide 9: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Simulation 1
Constant temperature and
constant charging/ discharging current
SoC and R0 estimation
SoH estimation with ageing

## Slide 10: SoC/SoH Estimation by an Adaptive Observer
El Lakkis, Mohamad, et al. "Combined battery SOC/SOH estimation using a nonlinear adaptive observer." 2015 European Control Conference (ECC). IEEE, 2015.
Simulation 2
The current used is a charging/ discharging driving cycle for an electrical vehicle available at the Politecnico di Milano
Charging/ discharging driving cycle
Validation of the proposed observer